Math 316

Spring 04

set V

Solutions

3.4 p.192 (1*,10*,14*,16*,23*)

7.1 p.444(5*,21*,25*,28*,35*)

3.4.1 (192) Determine the period and frequency of the simple harmonic motion of a 4-kg mass on the end of a spring with spring constant 16 N/m.

Solution: We have

and

3.4. 10 (192) Consider a floating cylindrical buoy with radius , height  and uniform density  (recall that the density of water is ). The buoy is initially suspended at rest with its bottom at the top surface of the water and is released at time . Thereafter it is acted on by two forces: a downward gravitational force equal to its weight  and an upward force of buoyancy equal to the weight  of water displaced, where  is the depth of the bottom of the buoy beneath the surface at time  (Fig. 1). Conclude that the buoy undergoes simple harmonic motion around its equilibrium position  with period . Compute  and the amplitude of the motion if ,  and .

Solution: Balance of forces gives

Figure 1

which is simplified to the ODE

The particular solution is  as can be easily verified by looking for the equilibrium solution: set  to get . Then we look for the solution in the form  so that the homogeneous solution  satisfies

so that  with . The general solution is then

. Satisfying IC:

.

Finally:                                                        .

The amplitude is

and the period

where we have included  in all formulas to get the units right (of course, since it is equal to 1, one could carry out all manipulations without units and get the right answer, since all work is done in the CGS system of units.

3.4. 10 (193) Suppose that the mass in a mass-spring-dashpot system with , , and  is set in motion with  and . (a) Find the position function  and graph it. (b) Find the pseudoperiod of the oscillations and the equations of the ‘envelope curves’.

Solution: The equation of motion is  with solution  where  and .  Satisfying the IC we have

In order to graph this function and its envelope, we reduce first to the combined form

,

We graph this with the matlab script

» msd_system1(25,10,226,0,20,20,41)

pseudoperiod T = 2.094e+000 Amplitude = 2.500e+001  delta = 6.435e-001

%script for graphing the solution to a mass-spring-dashpot

% system and its envelope

function msd_system1(m,c,k,t0,t1,x0,v0)

%m mass; %k springconstant; c damping; t0/t1 start/end time

% x0 initial displacement; v0 initial velocity

t = linspace(t0,t1,100);

p = c/(2*m);

omega0 = (k/m)^.5;

omega = ((k/m)-p^2)^.5;

T = 2*pi/omega;

C1 = x0;

C2 = (v0+C1*p)/omega;

A=(C1^2+C2^2)^.5;

delta = atan(C2/C1);

disp(sprintf('pseudoperiod T = %5.3e Amplitude = %5.3e  delta = %5.3e ',...

T,A,delta))

y1 = A*exp(-p*t);

y2 = -A*exp(-p*t);

x =y1.*(cos(omega*t-delta));

plot(t,x,t,y1,'.',t,y2,'.')

xlabel(' time t')

ylabel('x(t)')

3.4. 16 (194) Suppose that the mass in a mass-spring-dashpot system with , , and  is set in motion with  and .  Find the position function  and determine whether the motion is overdamped, critically damped or underdamped. If it is underdamped write the solution in amplitude-phase form. Also find the undamped position function that would result if all was the same but the damping constant is set to zero. Graph the two solutions and compare.

Solution: For the original system, we have:

,  so that  and the system is overdamped.

Then, we can write the solution as  with

and . To determine the constants:

so that

.

For this type of problem, the following script is helpful

(it can handle all cases, so it can be used to work all problems in this subsection)

» msd_system2(3,30,63,0,1,2,2)

omega0 = 4.583e+000  p = 5.000e+000

system is overdamped

p1 = -3.000e+000  p2 = -7.000e+000  C1 = 4.000e+000  C2 = -2.000e+000

% Problems 15-21

%script for graphing the solution to a mass-spring-dashpot

% system and its envelope; this version treats all cases

function msd_system2(m,c,k,t0,t1,x0,v0)

%m mass; %k springconstant; c damping; t0/t1 start/end time

%x0 initial displacement; v0 initial velocity

t = linspace(t0,t1,100);

p = c/(2*m);

omega0 = (k/m)^.5;

disp(sprintf(' omega0 = %5.3e  p = %5.3e ',omega0,p))

% undamped analog

U1 = x0;

U2 = v0/omega0;

AU = (U1^2+U2^2)^.5;

deltau = atan(U2/U1);

xu = AU*cos(omega0*t-deltau);

if omega0 >= p % decide if it is underdamped

omega = ((k/m)-p^2)^.5;

disp(sprintf(' omega = %5.3e ',omega))

if omega0 == p then % this means it is critically damped

disp('system is critically damped')

% solution is x(t) = exp(-p*t)*(C1 + C2*t)

C1 = x0;

C2 = v0+p*x0;

x = exp(-p*t).*(C1 + C2*t);

plot(t,x,t,xu,'k')

xlabel(' time t')

ylabel('x(t)')

else

disp('system is underdamped')

% Now x(t) = exp(-pt)*(C1*cos(omega*t)+C2*sin(omega*t))

T = 2*pi/omega;

C1 = x0;

C2 = (v0+C1*p)/omega;

A=(C1^2+C2^2)^.5;

delta = atan(C2/C1);

disp(sprintf('pseudoperiod T = %5.3e Amplitude = %5.3e  delta = %5.3e ',...

T,A,delta))

y1 = A*exp(-p*t);

y2 = -A*exp(-p*t);

x =y1.*(cos(omega*t-delta));

plot(t,x,t,y1,'.',t,y2,'.',t,xu,'k')

xlabel(' time t')

ylabel('x(t)')

end

else

disp('system is overdamped')

% x(t) = C1*exp(p1*t) + C2*exp(p2*t)

pp = (p^2-omega0^2)^.5;

p1 = -p + pp; p2 = -p-pp;

det = -2*pp;

C1 = (x0*p2-v0)/det;

C2 = (v0-x0*p1)/det;

disp(sprintf('p1 = %5.3e  p2 = %5.3e  C1 = %5.3e  C2 = %5.3e',p1,p2,C1,C2))

x = C1*exp(p1*t)+C2*exp(p2*t);

plot(t,x,t,xu,'k')

xlabel(' time t')

ylabel('x(t)')

title('overdamped case')

end

3.4. 23 (194)  This problem deals with a highly simplified model of a car of weight 3200lb (mass = 0.375 slugs in fps units). Assume that the suspension system acts like a single spring and its shock absorbers like a single dashpot, so that its vertical vibrations satisfy  with appropriate values of the coefficients. (a) Find the stiffness coefficient k of the spring if the car undergoes free vibrations at 80 cycles per minute when it shock absorbers are disconnected. (b) With the shock absorbers connected the car is set into vibration by driving it over a bump, and the resulting damped vibrations have a frequency of 78 cycles/min. After how long will the time-varying amplitude be 1% of its initial value?

Solution: This problem is about using the values of the natural frequency  and damped frequency  which are

easily measured to determine the spring stiffness  and damping factor p.

We have

Also,

so that the time varying amplitude is given by

2.47s

7.1. 5 (444) Apply the definition to compute the Laplace transform of .

Solution: First we derive the answer with Matlab (for fun!)

» F=laplace(sinh(t))

F = 1/(s^2-1)

Now we do it honestly:

7.1. 21 (444) Find the Laplace transform using the table for .

Solution: Matlab answer:

» F=laplace(t*cos(2*t))

F  =  -1/(s^2+4)+2*s^2/(s^2+4)^2

We have ; we will use the shift formula

which, for and for  gives:

, , so that, combining

7.1. 25 (444) Find the inverse transform for

Solution: Matlab answer:

» f=ilaplace(1/s-2/s^(5/2))

f =1-8/3*t^(3/2)/pi^(1/2)

But  so that finally

7.1. 28 (444) Find the inverse transform for

Solution: Matlab answer:

» f=ilaplace((3*s+1)/(s^2+4))

f = 3*cos(2*t)+1/2*sin(2*t)

We have

7.1. 35 (444) Use the tabulated integral

to obtain  directly from the definition.

Solution: